## Slide 1
Final Report : Amphibious Bicycle Kit
BRITTANY STUART ● ALEX HEIN ● ABHIJITH RAVISHANKAR ● STEPHEN BURD

## Slide 2: Overview
Research Overview and Problem Statement
Concept Generation
Product Design and Function
Engineering Analysis and Design for Assembly
Manufacturing and Materials
Comparison to Benchmarks
Economic Analysis
Notes: Problem Statement - Brittany
Customer Research - Brittany
Market Research – Alex
Product Research –Alex
Patent Research – Stephen and Ahbi
House of Quality - Stephen
Problem Definition -- Ahbi
Questions – All of us

## Slide 3: Research
Market Research
  VQDT found out that 96.8 million people are affected by floods annually. The poor and rural areas of cities are largely affected by this disaster.
Customer Research
  In addition to the cost and widespread affects, one of the biggest complications associated with flooding is lack of available transportation to safer locations in areas with no immediate aid.
Patent Research
  The existing paddle boat was very expensive. This would limit the market size as cost would become a factor.

## Slide 4: Problem Definition
Updated problem definition
  The transportation of people in post-flood situations using attachments to a bicycle. This is concentrated to people in rural and poor areas.
  Creating a list of materials and manufacturing parts required in the Bill Of Materials, making CAD models for our attachments and analyzing an economic model of the design.

## Slide 5: Results of Problem Definition
Low cost
Light Weight
Easy to use
Low maintenance
Durable
Takes less than five minutes to install
Supports up to 115 kilograms
Takes less than 60 seconds to deploy

## Slide 6: Concept Generation (Chart 1: Function Tree)
Transport people in floods
Keep afloat
Move forward
Turn
Transform between water and land modes
Produce buoyancy
Allow stability
Resist water
Dampen oscillations
Prevent tip-overs
Increase surface area
Move in water
Rotate turning system
Deploy
Retract
Deploy turning system
Deploy propulsion system
Deploy floatation system
Retract turning system
Retract propulsion system
Retract flotation system
Propel forward

## Slide 7: Concept Generation (Chart 2: Morphological Chart)
Functions | Possible Solutions |  |  |  | 
Turning | Back Rudder | Front Rudder |  |  | 
Increase Surface Area | Pontoon | Ripcord Floats | Stabilizers | Pool Noodle | 
Resist Water | Silicone Spray | Zinc Powder Coat | Paint | PVC Parts | 
Propel Forward | Fins in Spokes | Sail | Enclosed Propeller | Open Propeller | Paddle
Maneuver Through Water | Front Wedge |  |  |  | 
Deploy/Retract Floatation | Ripcord | Zip Tie | Snaps | Hand Pump | Motor Pump
Deploy/Retract Propulsion | Slip Fins into Spokes | Fold Fins out of Spokes | Mount Propeller On Wheel |  | 
Prevent Tipping | Wide Base | Square Pontoon Base | Triangle Pontoon Base | Ring of Pool Noodles | 

## Slide 8: Final Concept
Front Rudder
Clamp
Inflatable Pontoon
T – Base
Pump
Front Wedge
Front Rudder
Paint
Snaps
Rip Cord
Triangle Base
Fold Fins
Front Wedge
Final Concept: Primary Concept:
  Datum Concept
  Front Rudder
  Paint
  Clamps
  Inflatable Pontoon
  Square Base
  Propeller

## Slide 9: The Design: Front Unit
Connects to bicycle on front axle and on steering column
Has support for pontoons
Comes to point at front, acting as wedge
Disk is inserted into front tire
Unit rotates as steering column is rotated, acting as a rudder

## Slide 10: The Design: Rear Unit
Attaches to bicycle on rear axle and seat post
Has support for pontoons

## Slide 11: The Design: Centrifugal Pump
Rotates as pedals are rotated
Additional gear is mounted to chain to drive a second axle
This axle drives another chain which drives the pump
Forced rotation of fins inside of pump accelerates internal water velocity
Water exits pump at maximum speed, forcing bicycle in opposite direction

## Slide 12: The Design: Pontoons
Flexible PVC inflatable tubes
Have standard valve stems for use with bicycle tire pumps

## Slide 13: Concept: Front Wedge
Function
  Moving debris from path
How it works
  Forms wedge to cut through water
Model Findings
  Can be helpful in steering
  Must be made of thin metal
Diagram: Laminar Flow

## Slide 14: Concept: Front Rudder
Function
  To allow the bicycle to turn
How it works
  Using the surface area created
Model Findings
  Consider using hollow rudder
  Rudder adds 3.2kg of mass
Front Rudder
Noise
Waves
Current
Control
Velocity
Surface Area
Input
Turn Steering Column
Output
Direction Change
P-Diagram: Front Rudder

## Slide 15: Concept: Centrifugal Pump
Function
  Enclosed fin system
  Water cycles within case and forced out one outlet.
How
  Fins are attacked to rear wheel
  Pressure from fins and case’s cylindrical shape causes water to flow in circle
  Water is released at one outlet for maximum speed
Model Findings
  Most energy is conserved in this method for weight purposes
Diagram: Centrifugal Pump

## Slide 16: Concept: Flotation Device
Function
  To provide a buoyant force for the whole device
How
  Airtight compartment fills with air to provide buoyant force while in water
Input
Volume of floatation device
Noise
Weight of bicycle
Weight of user
Salinity of water
Temperature of water
Output
Buoyant force
Control Factors
Size of floatation device
Shape of floatation device
Flotation Device
P-Diagram: Flotation Device

## Slide 17: Design for Assembly
Chart: 
| Overall Assembly | Part Retrieval | Part Handling | Part Mating | Total Score
Trial One | 12 | 8 | 12 | 10 | 42
Trial Two | 20 | 8 | 14 | 16 | 58

## Slide 18: Materials
Aluminum 6061
  Pipes and Front Wedge
    Corrosion Resistant
    Easy to manufacture with (bend)
    Light Weight
    Lower Cost
PVC 10 oz. Fabric
  Pontoons
    Water Resistant
    Tear and Puncture Resistant
    Similar material used on inflatable life rafts
ABS plastic
  Pump
    Easy to manufacture with
    Water Resistant
Chart: Chart 3: Use of Material by Mass
| Aluminum 6061 | PVC 10 oz Fabric | ABS Plastic | Other
Sales | 4 | 3 | 2.5 | 0.5

## Slide 19: Manufacturing
Fin (x4)
Fin Center
Axle
Pump Case Right
Pump Case Left
Pontoons
Cut Fabric
Sew Fabric
Front Wedge
Bend Sheet Metal
Drill Holes for Mounting
Mounts
Cut Pipes to Length
Bend Pipes
Weld on Axle Mounts
Drill Holes and Chamfer
Pump
CNC Mill pump case and fins
*only assembly is the pump and case
Chart 4: Pump Assembly Flow Diagram

## Slide 20: Comparison to Benchmarks
The Shuttle Bike is the only comparable product on the market
Costs $5000
Can be stored in backpack
Takes 15 minutes to deploy
Not amphibious

## Slide 21: Economic Analysis
Pay Back Period:7th Quarter
Net Present Value: $294k
Min production: 1061
Return on Investment: 74%

## Slide 22: Questions
Alex Hein – heina@purdue.edu
Stephen Burd – sburd@purdue.edu
Brittany Stuart – stuartb@purdue.edu
Abhijith Ravishankar – ravishan@purdue.edu

## Slide 23: References
[1] Eric Guyer (2011). Expert Witness Painting Aluminum – Paint Failure and Defects. Retrieved from http://www.the-coatings-expert.com/painting-aluminum.htm
[2] SBK-KIT (2014). Shuttle Bike. Retrieved from http://www.shuttlebike.it/index.html